## Slide 1
Magnetic Field Control and Monitoring for
The ACME III Electron Electric Dipole Moment Search
Xing Fan, Siyuan Liu, Maya Watts, Ayami Hiramoto, Daniel G. Ang, David DeMille, Collin Diver, John M. Doyle, Gerald Gabrielse, Zhen Han, Peiran Hu , Nick R Hutzler, Zack Lasner, Takahiko Masuda, Cole Meisenhelder, Cris D Panda, Satoshi Uetake, Xing Wu, Koji Yoshimura
X05.00005
2024 Jun 4 DAMOP, Fort Worth, Texas

## Slide 2: Electron’s Electric Dipole Moment as a BSM CP probe
spin
spin
unit: charge×length
de･s>0
de･s<0
X
ΦCP
e-
e-
for ΦCP~1, sensitive to ~30TeV
time-reversal

## Slide 3: Principle of EDM measurement
or
E
Apply an electric field
e-
e-
de
spin precession energy
Experimentally
E
spin precession
precession time
# of measured spins
→

## Slide 4: ACME’s Molecule: ThO
Th2+
O2-
Eeff~80GV/cm
huge flux by Cryogenic Buffer Gas Beam (CBGB) = high N
Eeff=80 GV/cm
3Δ1 state : long τ and B-insensitivity
http://doylegroup.harvard.edu/edm
e-

## Slide 5: The ACME Experiment
magnetic shield
Eext bias plate
spin prep
spin readout
flow
Th2+
O2-
e-
Eext
many
many
many
ThO

## Slide 6
ACME I (2014) |de| < 8.7×10-29 e•cm
Science 343, 269 (2014)

## Slide 7
ACME II (2018) |de| < 1.1×10-29 e•cm
ACME I (2014) |de| < 8.7×10-29 e•cm
Nature 562, 355 (2018)

## Slide 8
ACME II (2018) |de| < 1.1×10-29 e•cm
ACME I (2014) |de| < 8.7×10-29 e•cm
ACME III (2025?) |de| < 0.03?×10-29 e•cm
x5 longer coherence time
new photon counter
D.G.Ang, et al, Phys. Rev. A 106, 022808(2022)
X Wu, et al, New J. Phys. 24 073043(2022)
A. Hiramoto, et al, NIM A, 1045, 167513(2022)

## Slide 9: Magnetic Field Control
3-layer magnetic shield
3000 lbs = 1500kg
3,600 wire connections
<30μG without active cancellation
<5μG with active cancellation
1.5m
2m
E
spin precession
B
Bearth=500mG ↔︎de=10-24 e･cm
(target: de=10-30 e･cm)
*ThO 3Δ1 state and switching help a lot

## Slide 10: Degaussing
after assembling
large magnetization
→large residual B field
small residual B field

## Slide 11: Degaussing Coil
degaussing coils
shield

## Slide 12: Degaussing Coil
degaussing coils
degaussing freq <1Hz
current offset in degaussing is very important! (<1mA)

## Slide 13: Low Fringe-Field Magnetic Field Coil
0.33% homogeneity over 100cm
8 sub-coils
able to cancel up to linear order gradient
B
ThO
cosθ coil + artificial return yoke

## Slide 14
ThO
prep
readout
Aluminum chamber
fluorescence collection lens
>30% solid angle!
E-field plates
ITO-coated fused silica
low non-reversing E
low mounting stress
non-magnetic
ThO
Ebias

## Slide 15: The Whole Beamline
ThO
Cryogenic
Buffer Gas Source
molecular
lens
aluminum chamber
prep
readout
YAG
molecule pulse spacial length ~1m
50 Hz rep rate
X Wu, et al, New J. Phys. 24 073043(2022)

## Slide 16: Magnetic Field Coil On
ThO
coil
Bx, By, Bz + linear gradient

## Slide 17: Magnetic Shield On
ThO
SiPM
x1.8 higher Q.E.
A. Hiramoto et al NIM A 1045 167513 (2022)

## Slide 18: And Many More Peripherals
vertical STIRAP
stage
optics cart
racks
racks
ThO

## Slide 19: Let There Be ThO Fluorescense!
x30 higher than ACME2
with x5 longer beamline!
Will start data-taking in 2024, probes ~100TeV scale
physics with ThO signal → next talk

## Slide 20: Many Thanks!
ACME Collaboration
David P DeMille
John M Doyle
Gerald Gabrielse
Zack Lasner

## Slide 22: Degaussing Needs to be <1Hz
0.1Hz
0.3Hz
1Hz
3Hz
10Hz
30Hz