## Slide 1
After precession, the final state is projected to a pair of orthogonal basis vectors using a 703 nm probe laser (on the H-I transition) with linear polarization rapidly switched (200 kHz) between x and y.
We collect the 512 nm fluorescence as the molecules decay back to the ground state.
ACME III planned improvement: upgrade PMTs to silicon photomultipliers (SiPMs) and optimize collection optics
SiPM characterization tests have been performed
1. Buffer Gas Beam Source
Produce ThO molecules through pulsed ablation of a ceramic ThO2 target at 50 Hz
Neon buffer gas thermalizes the molecules. Molecule beam is cooled to 4 K
~1011 molecules/sr in the electro-vibrational ground state.
Rotational cooling transfers more population to the level.
9 cm
Beamline
Ablation
window
16 K
4 K
Neon
flow
line
1.5 cm
Motivation & Theory
Permanent EDMs violate T-symmetry.
Many theories beyond the Standard Model predict T violation and EDMs at current experimental precision.
Key EDM results since 2010. Two-loop sensitivity from Nakai & Reece (2017).
One-loop sensitivity from Feng (2013). LHC scale gives stop mass sensitivity.
Beyond the ACME II Limit on the Electron EDM
References
ACME II result: V Andreev et al., Nature 562, 355-360 (2018)
ACME I result: J Baron et al., Science 343, 269-272 (2014)
ACME I detailed report: J Baron et al., New J. Phys.19 (2017)
Eeff Calculations: L. V. Skripnikov et al., J. Chem. Phys. 142 024301 (2015), T. Fleig et al., J. Mol. Spec. 300:16-21 (2014)
EDM & SUSY: J. Feng, Annu. Rev. Nucl. Part. Sci., 63:35, 1-82 (2013), Y. Nakai, et al., J. High Energy Phys. 2017:31 (2017)
Interpreting the Electron EDM Constraint: C. Cesarotti et al., J. High Energ. Phys. 2019:59 (2019)
Noise Reduction
ACME II had 1.7 times more noise than expected at the shot noise limit
This noise was determined to come from both timing error in the data acquisition system and a timing offset between polarization bins
ACME III demonstrated improvement: We were able to suppress this noise by controlling both parameters
ACME III planned improvement: Reduce noise from velocity fluctuations by applying smaller magnetic fields
New magnetic shield designs will need to reduce ambient fields to 1 µG and gradients to < 1 µG/cm
5. State Readout
ACME III Apparatus
ACME Collaboration: Cole Meisenhelder1, Daniel Ang1, Vitaly Andreev1, James Chow2, David DeMille2, John Doyle1, Gerald Gabrielse3, Jonathan Haefner1, Zhen Han2, Nicholas Hutzler4, Zack Lasner2, Takahiko Masuda5, Brendon O’Leary2, Cristian Panda1, Satoshi Uetake5, Adam West2, Elizabeth Petrik West1, Xing Wu1,2, Koji Yoshimura5
Affiliation: 1Harvard University, 2Yale University, 3Northwestern University, 4California Institute of Technology, 5Okayama University
3. State Preparation
STIRAP coherently transfers population to experimental H-state with ~75% efficiency (ACME II)
ACME III planned improvement: perform STIRAP horizontally through the X-A-H states (1892 nm, 943 nm), which will allow better suppression of systematics caused by birefringence gradients
703 nm cleanup laser reprojects the state onto a coherent superposition of states
STIRAP Level Structure
Cleanup Level Structure
ACME III planned improvement: Improve collimation of molecular beam by applying a hexapole electric field
Requires compact rotational cooling to maximize input flux
Molecules are transferred efficiently from the ground state (X) to the lensing state Q and back using X-C-Q STIRAP
Demonstrated double STIRAP efficiency >75%
Expected increase of molecular flux by a factor of 15 vs. ACME II
+
+
+
-
-
-
E
2. Molecular Lens
SUSY particle bounds from this result.
Fig. from Matt Reece (unpublished)
ACME III projection () dashed.
4. State Precession
The molecules in the prepared state acquire phase as they fly through the electric and magnetic fields of the interaction region.
ACME III planned improvement: Recent measurements determined that the lifetime of the H-state is 4-6 ms, allowing us to increase precession time by a factor of 4-6 compared to ACME II (improved lifetime measurements are underway)
Increased precession time decreases solid angle that reaches the detection region (see table below)
Molecular lens will help to counteract this loss
Requires new interaction region design to accommodate increased length
Systematic Search & Characterization
Improvement | Signal Gain | EDM Sensitivity Gain
Increased precession time | 0.20 | 2.3
Electrostatic lens | 20.5 | 4.5
SiPM detector upgrade | 2.3 | 1.5
Timing jitter noise reduction* | 1 | 1.7
Total | 9.4 | 26.4
ACME II daily statistical sensitivity |  | 
Projected ACME III daily sensitivity |  | 
Improvement | Signal Gain | EDM Sensitivity Gain
Increased precession time | 0.20 | 2.3
Electrostatic lens | 20.5 | 4.5
SiPM detector upgrade | 2.3 | 1.5
Timing jitter noise reduction* | 1 | 1.7
Total | 9.4 | 26.4
ACME II daily statistical sensitivity |  | 
Projected ACME III daily sensitivity |  | 
Overall projected sensitivity
In ACME II, we varied 40 different experiment parameters in the search for systematic errors (e.g. electric & magnetic fields, laser powers, detunings, pointing, polarization, molecular beam clipping, experiment timing, and analysis parameters)
Where possible, we intentionally exaggerate the parameter and assume depends linearly on the parameter. The systematic error under optimal conditions is given as
The final contribution to the systematic uncertainty is computed from the linear error propagation of the two variables and .
ACME III planned improvement: further suppress systematics related to using improved electric field plates and horizontal STIRAP
ThO: effective electric field
ACME II parameters:
  Precession time
  Measurement contrast
  Detected molecule flux
  Result:
*Already implemented
 | Requirement | Measured Value
Photon Detection Efficiency | ~ 50% | 2.5 x PMT
Dark Count Rate | < 10 Mcps | < 10 Mcps @ -10 °C
Cross Talk and After Pulse | < 25% | ~ 15%